## Slide 1: Hands-on training for the Core Imaging Library (CIL)
an open-source reconstruction platform for challenging and novel data.
Gemma Fardell – STFC
Jakob Sauer Jørgensen – DTU
Laura Murgatroyd – STFC
Danica Sugic – STFC
Hannah Robarts - STFC
Evangelos Papoutsellis – Finden
Edoardo Pasca – STFC
Margaret Duff – STFC
Franck Vidal – STFC
Casper da Casta-Luis - STFC
Whilst you’re waiting for us to get started, have a think about the strangest dataset you’ve ever come across, we’ll ask you to share with the group as an ice breaker

## Slide 2: Hands-on training for the Core Imaging Library (CIL)
an open-source reconstruction platform for challenging and novel data.
Gemma Fardell – STFC
Jakob Sauer Jørgensen – DTU
Laura Murgatroyd – STFC
Danica Sugic – STFC
Hannah Robarts - STFC
Evangelos Papoutsellis – Finden
Edoardo Pasca – STFC
Margaret Duff – STFC
Franck Vidal – STFC
Casper da Casta-Luis - STFC

## Slide 3: Our goals with this course
Give an overview of CT data processing with CIL
Support you in trying out CIL with our Jupyter notebook demos on the cloud

## Slide 4: Training Program
Geometry, Data Reading and FBP/FDK Reconstruction – 1:10-1:45 (Lead: Franck)
Icebreaker
Introduction to CT and FBP
Introduction to CIL
Cloud setup
Notebook demonstration: 1_Introduction/01_intro_walnut_conebeam.ipynb
Pre-processing – 1:45-2:30 (Lead: Laura)
Introduction to pre-processing
Notebook: 1_Introduction/02_intro_sandstone_parallel_roi.ipynb
Break
Introduction to Iterative Reconstruction - 2:45-3:45 (Lead: Franck)
Introduction
Notebook: 1_Introduction/04_FBP_CGLS_SIRT.ipynb
Break
Time to explore and discuss – 4:00-4:50 (Lead: Laura)
  Introduction
  Option A: Further Pre-processing
  Option B: Geometry
  Option C: Iterative Reconstruction
Conclusions 4:50-5:00
  - Feedback (post its)
Notes: Same breakout rooms (groups of 5ish) for all 3 sessions.
Jakob and Franck – hosts on Monday

## Slide 5: Icebreaker
Please:
Introduce yourself and your background
Explain what you want to get out of the training
Tell the group about the strangest dataset you have ever come across

## Slide 6: CT and FBP

## Slide 7: Tomography

## Slide 8: Tomography

## Slide 9: Beer-Lambert Law
?
Reconstructed volume:
map of linear attenuation coefficients (µ)
often expressed in cm-1

## Slide 10: Preparing raw data for the reconstruction
Raw image
Detectors are not perfect
Defects build up over time
Non uniform spread of intensity across the detector

## Slide 11: Flat-field correction
Raw image
Flat-field corrected image

## Slide 12: Flat and dark field correction

## Slide 13: Flat-field correction: How does it work?
Image | Sample | Beam
raw | with | on
dark field | without | off
white field | without | on
corrected | with | on

## Slide 14: Flat-field correction: How does it work?
corrected image
raw
dark field
light field

## Slide 15: Minus log

## Slide 16: Take many projections
An x-ray radiograph of a shell measured at the University of Helsinki [1]
[1] Kamutta, E., Mäkinen, S., & Meaney, A. (2022). Cone-Beam Computed Tomography Dataset of a Seashell (1.1.0) [Data set]. Zenodo. https://doi.org/10.5281/zenodo.6983008

## Slide 17: Sinogram: How the attenuation changes as we rotate the object
The shell has a much more complex sinogram

## Slide 18: Filtered Back Projection (FBP)

## Slide 19: Filtered Back Projection (FBP)
Unfiltered
Courtesy J. Jørgensen

## Slide 20: Filtered Back Projection (FBP)
Courtesy J. Jørgensen

## Slide 21: Filtered Back Projection (FBP)
Filtered
Unfiltered
Courtesy J. Jørgensen

## Slide 22: Filtered Back Projection (FBP)
Pros
Fast as based on FFT and backprojection
Few parameters
Typically works very well
Reconstruction behaviour well understood

## Slide 23: What is the Core Imaging Library?
A Python library for processing and reconstruction of tomography data.
Optimised standard methods, such as Filtered Back Projection
Special emphasis on challenging data sets: noisy, non-standard, incomplete, multi-channel, ...
Highly modular to allow creation of bespoke pipelines.
Apache v2 license.
Actively developed on GitHub: https://github.com/TomographicImaging/CIL

## Slide 24: Core Imaging Library for CT and other inverse problems
data = ZEISSDataReader(filename).read()
data = TransmissionAbsorptionConverter()(data)
show_geometry(data.geometry)
recon = FDK(data).run()
show2D(recon)
Data readers/writers
Pre-processing tools
Image reconstruction
Near math optimisation syntax
Visualisation
2D, 3D and 4D data
TIGRE and ASTRA backend
ccpi.ac.uk/CIL

## Slide 25: Who is CIL for?
CT experimentalists
  Optimised standard algorithms for large data
  Batch processing
  To utilise reconstruction algorithms for poor data quality or to handle novel imaging modalities
Image processing specialists
  To easily implement new reconstruction algorithms
  Assess them against existing ones.

## Slide 26: CIL Module Structure and Contents
Jørgensen et al. 2021: Core Imaging Library - Part I: a versatile Python framework for tomographic imaging, Phil. Trans. R. Soc. A, 379, 20200192: https://doi.org/10.1098/rsta.2020.0192
The cil.plugins module contains wrapper code for other software and third-party libraries that need to be installed separately to be used by CIL.
recon
FBP/FDK

## Slide 28: Documentation
https://tomographicimaging.github.io/CIL

## Slide 29: CIL Module Structure and Contents
Jørgensen et al. 2021: Core Imaging Library - Part I: a versatile Python framework for tomographic imaging, Phil. Trans. R. Soc. A, 379, 20200192: https://doi.org/10.1098/rsta.2020.0192
recon
FBP/FDK
iterative
PDHG+TV

## Slide 30: Example: Walnut reconstruction! CIL-Demos/examples/1_Introduction /01_intro_walnut_conebeam.ipynb
Learning Objectives:
Load and investigate a ZEISS data set.
Apply CIL's TransmissionAbsorptionConverter.
Compute FDK reconstruction using CIL and compare with a reconstruction made from fewer projections.
Write out the reconstructed image to a TIFF stack.

## Slide 31: Questions?

## Slide 32: Training Program
Geometry, Data Reading and FBP/FDK Reconstruction – 1:10-1:45 (Lead: Franck)
Icebreaker
Introduction to CT and FBP
Introduction to CIL
Cloud setup
Notebook demonstration: 1_Introduction/01_intro_walnut_conebeam.ipynb
Pre-processing – 1:45-2:30 (Lead: Laura)
Introduction to pre-processing
Notebook: 1_Introduction/02_intro_sandstone_parallel_roi.ipynb
Break
Introduction to Iterative Reconstruction - 2:45-3:45 (Lead: Franck)
Introduction
Notebook: 1_Introduction/04_FBP_CGLS_SIRT.ipynb
Break
Time to explore and discuss – 4:00-4:50 (Lead: Laura)
  Introduction Option A: Further Pre-processing
  Option B: Geometry
  Option C: Iterative Reconstruction
Conclusions 4:50-5:00
  - Feedback (post its)
Notes: Same breakout rooms (groups of 5ish) for all 3 sessions.
Jakob and Franck – hosts on Monday

## Slide 33: Centre of Rotation Correction
CoR: The projection of the axis of rotation onto the detector
Reconstruction assumes axis of rotation is horizontally centred on detector
Offset introduces blurring and artifacts
We correct for this by updating our geometry
Parallel Beam
Notes: The centre of rotation is the projection of the axis of rotation on to the detector. The reconstruction assumes this is horizontally centred on the detector. An offset introduces blurring and artefacts in the reconstruction.
Can crop detector if parallel beam, restricts to whole pixel offset and also doesn’t work for fan beam. By updating the geometry we can go to subpixel accuracy
‘tuning-fork’ style artifacts.
So how do we find out how big this offset is?

## Slide 34: Centre of Rotation in CIL – X Correlation
cil.processors.CentreOfRotationCorrector.xcorrelation(slice_index='centre’, projection_index=0, ang_tol=0.1)
For parallel beam geometry
Requires two rows 180 degrees apart
Notes: Need redundant data, only redundancy is 0 and 180

## Slide 35: Centre of Rotation Correction
Cone/Fan Beam
Non-centred
Centred
Notes: So now coming on to the fan or cone beam case, remember we’re looking at the projection of the axis of rotation on to the detector.
magnification and fan angle
Full scan

## Slide 36: Centre of Rotation in CIL – Image Sharpness
cil.processors.CentreOfRotationCorrector.image_sharpness(slice_index='centre’, backend='tigre', tolerance=0.005, search_range=None)
Reconstructs with FBP/FDK a single slice and adjusts the centre of rotation offset to maximise the sharpness
By default the search range is ¼ width of the detector panel
For parallel beam or centre-slice cone beam
Works best with full 360 degree data
Can only be used on datasets that can be reconstructed with FBP/FDK
https://tomographicimaging.github.io/CIL/nightly/processors/#cil.processors.CentreOfRotationCorrector.image_sharpness
Notes: Maximise sharpness and getting rid of blurr
Redundant data
tolerance (float, default=0.005) – The tolerance of the fit in pixels, the default is 1/200 of a pixel. This is a stopping criteria, not a statement of accuracy of the algorithm.

## Slide 37: Centre of Rotation Correction in CIL - Manual
AcquisitionGeometry’s .get_centre_of_rotation()
{'offset': (0.1, 'units distance'), 'angle': (0.0, 'radian’)}
.set_centre_of_rotation(offset)
In CIL, the centre of rotation offset is defined as the offset from the centre of the detector panel
Notes: To go about manually setting the centre of rotation correction in CIL, the best place to start is by looking at the current CoR offset. Do this by printing get_centre_of_rotation

## Slide 38: Region of Interest Correction
The object is too large to fit in the field of view, or we want a close view of a specific ROI
The projections are truncated – don’t cover entire width of object and are contaminated by data exterior to the ROI.
Reconstruction of ROI will also be contaminated.

## Slide 39: Region of Interest correction
Scan with whole sample in field of view (then cropped)
ROI scan: with only circle in field of view
Sample
Large artifact in ROI scan – white ring
To correct this we pad the data an amount roughly the width of the object
cil.processors.Padder
Notes: Boundaries are correct

## Slide 40: Region of Interest correction
Scan with whole sample in field of view (then cropped)
ROI scan: with only circle in field of view
Sample
Corrected by padding ROI scan

## Slide 41: Region of Interest correction
Cropped full scan
ROI scan
Sample

## Slide 42: Region of Interest correction
Cropped full scan
ROI scan
Sample
Cropped full scan
Corrected ROI scan

## Slide 43: Region of Interest correction
Padding provides great improvement but can’t fully recover intensities
Contamination from outside the ROI provides even greater problem with iterative reconstruction.
Notes: This is because with our analytical recon we’re only doing one backprojection.
With iterative we’re doing multiple so the contamination builds up

## Slide 44: Many other artifacts
Ring artifacts
Cone beam artifacts
Beam hardening
Misalignment
Motion
And more!
F.P. Vidal et al. Investigation of artefact sources in synchrotron microtomography via virtual X-ray imaging, Nuclear Instruments and Methods in Physics Research Section B: Beam Interactions with Materials and Atoms, Volume 234, Issue 3,
2005, Pages 333-348, ISSN 0168-583X,
https://doi.org/10.1016/j.nimb.2005.02.003
Notes: Scatter
Cone beam artifacts

## Slide 45: BREAK

## Slide 46: Guess the object

## Slide 47: The next slide reveals the answer!

## Slide 48: Guess the object
Reconstruction - slice
Reconstruction - slice
Projection

## Slide 49: Sandstone Data
The Scan:
Parallel Beam
0 to 180 degrees
ROI
Centre of Rotation – which algorithm would you expect to use?
Look out for centre of rotation and ROI artifacts!

## Slide 50: Log in to Jupyter Hub
Go to the link provided
Enter the username and password on your slip of paper
Wait for the server to start up
Check you can see the CIL-Demos folder

## Slide 51: Killing kernels – IMPORTANT

## Slide 52: Try out the Sandstone notebook
Go to: CIL-Demos/demos/1_Introduction/02_intro_sandstone_parallel_roi.ipynb
Learning Objectives:
Load and investigate a real data set.
Determine geometric information of the data and set up CIL data structures.
Apply CIL processors to pre-process the data, including normalisation, negative log, region-of-interest and centre of rotation correction.
Compute FBP reconstruction using CIL and compare with reconstruction provided.

## Slide 53: Questions?

## Slide 54: Training Program
Geometry, Data Reading and FBP/FDK Reconstruction – 1:10-1:45 (Lead: Franck)
Icebreaker
Introduction to CT and FBP
Introduction to CIL
Cloud setup
Notebook demonstration: 1_Introduction/01_intro_walnut_conebeam.ipynb
Pre-processing – 1:45-2:30 (Lead: Laura)
Introduction to pre-processing
Notebook: 1_Introduction/02_intro_sandstone_parallel_roi.ipynb
Break
Introduction to Iterative Reconstruction - 2:45-3:45 (Lead: Franck)
Introduction
Notebook: 1_Introduction/04_FBP_CGLS_SIRT.ipynb
Break
Time to explore and discuss – 4:00-4:50 (Lead: Laura)
  Introduction
  Option A: Further Pre-processing
  Option B: Geometry
  Option C: Iterative Reconstruction
Conclusions 4:50-5:00
  - Feedback (post its)
Notes: Same breakout rooms (groups of 5ish) for all 3 sessions.
Jakob and Franck – hosts on Monday

## Slide 55: Iterative Reconstruction

## Slide 56: Filtered Back Projection (FBP)
Fast as based on FFT and backprojection
Few parameters
Typically works very well
Reconstruction behaviour well understood
Number of projections needed proportional to acquisition panel size
Full angular range required (limited angle problem)
Modest amount of noise tolerated
Fixed scan geometries
Cannot make use of prior knowledge such as non-negativity
Pros
Cons

## Slide 57: Imaging Model for Iterative Reconstruction
Assume the object is constant in each pixel
uj is the j-th pixel value
aij is the path length in the j-th pixel

## Slide 58: Imaging Model for Iterative Reconstruction
Extremely large set of linear equations
Iterative reconstruction is based on algorithms and optimisation problems

## Slide 59: Solve optimisation problem iteratively
28

## Slide 60: Solve optimisation problem iteratively

## Slide 61: Solve optimisation problem iteratively

## Slide 62: Solve optimisation problem iteratively

## Slide 63: Solve optimisation problem iteratively

## Slide 64: Solve optimisation problem iteratively

## Slide 65: Solve optimisation problem iteratively

## Slide 66: Questions?

## Slide 67: CIL module structure and contents
Jørgensen et al. 2021: Core Imaging Library - Part I: a versatile Python framework for tomographic imaging, Phil. Trans. R. Soc. A, 379, 20200192: https://doi.org/10.1098/rsta.2020.0192
recon
FBP/FDK
> v21.3

## Slide 68: CIL Optimisation module
TotalVariation

## Slide 69: Killing kernels – IMPORTANT

## Slide 70: Let's try that out
Go to: CIL-Demos/demos/1_Introduction/04_FBP_CGLS_SIRT.ipynb
Learning Objectives:
In the end of this session, participants will be able to:
formulate CT reconstruction as an optimisation problem and solve it iteratively
introduce constraints in the optimisation problem
visualise final and intermediate reconstruction results

## Slide 71: BREAK

## Slide 72: Training Program
Geometry, Data Reading and FBP/FDK Reconstruction – 1:10-1:45 (Lead: Franck)
Icebreaker
Introduction to CT and FBP
Introduction to CIL
Cloud setup
Notebook demonstration: 1_Introduction/01_intro_walnut_conebeam.ipynb
Pre-processing – 1:45-2:30 (Lead: Laura)
Introduction to pre-processing
Notebook: 1_Introduction/02_intro_sandstone_parallel_roi.ipynb
Break
Introduction to Iterative Reconstruction - 2:45-3:45 (Lead: Franck)
Introduction
Notebook: 1_Introduction/04_FBP_CGLS_SIRT.ipynb
Break
Time to explore and discuss – 4:00-4:50 (Lead: Laura)
  Introduction
  Option A: Further Pre-processing
  Option B: Geometry
  Option C: Iterative Reconstruction
Conclusions 4:50-5:00
  - Feedback (post its)
Notes: Same breakout rooms (groups of 5ish) for all 3 sessions.
Jakob and Franck – hosts on Monday

## Slide 73: Explore!
Further Pre-processing | 
Preprocessing Synchrotron Data | 1_Introduction/03_preprocessing.ipynb
Preprocessing Cone Beam Data | 1_Introduction/exercises/02_preprocessing_seeds_conebeam.ipynb
Paganin Phase Retrieval | 4_Deep_Dives/02_phase_retrieval.ipynb
Geometry | 
Where is my Reader? | 1_Introduction/exercises/03_where_is_my_reader.ipynb
Geometry | 1_Introduction/00_CIL_Geometry.ipynb
Iterative Reconstruction | 
FBP & SIRT | 1_Introduction/05_usb_limited_angle_fbp_sirt.ipynb
Gradient Descent & FISTA | 2_Iterative/01_optimisation_gd_fista.ipynb

## Slide 74: Regroup